ACPI vs FDT
Adding ACPI support to a driver with reference to similarities and differences with FDT

---
DTS for I2C
        i2c_0: i2c@12C60000 {
        compatible = "samsung,s3c2440-i2c";
        reg = <0x12C60000 0x100>;
        interrupts = <0 56 0>;
        #address-cells = <1>;
        #size-cells = <0>;
        samsung,i2c-slave-addr = <0x66>;
        gpios = <&gpb3 0 2 3 0>,
        <&gpb3 1 2 3 0>;
        };

---
ASL for I2C
        Device (I2C) {
        Name (_HID, "LINA0001")
        Name (_UID, 0)
        Method (_CRS, 0x0, NotSerialized) {
        Name (RBUF, ResourceTemplate ()
        {
        Memory32Fixed (ReadWrite, 0x12C60000,
        0x00000100)
        Interrupt (ResourceConsumer, Level,
        ActiveLow, Exclusive, , , ) {0x58}
        GpioIo (Exclusive, PullDefault, , , ,
        "\\_SB.GPB3") {0x2A, 0x2B}
        })
        Return (RBUF)
        }
        Method (DLAY, 0x0, NotSerialized) {
        Return (100)
        }
        Method (SADD, 0x0, NotSerialized) {
        Return (0x66)
        }
        Method (FREQ, 0x0, NotSerialized) {
        Return (20000)
        }
        }

---
ASL vs DTS
- DTS presented as key/value pairs
- ASL represented as “methods”
- ASL has by default “defines”
- ASL code is actually executed in interpreter

---
I2C Device Driver Example
- i2c-s3c2410.c driver used as example
- Actual system code defined by OEM ASL
- ASL binding here is just an example

---
ACPI Device Table
 MODULE_DEVICE_TABLE(of, s3c24xx_i2c_match);
 #endif
+#ifdef CONFIG_ACPI
+static const struct acpi_device_id s3c24xx_i2c_acpi_match[] = {
+ { "LINA0001", },
+ { }
+};
+MODULE_DEVICE_TABLE(acpi, s3c24xx_i2c_acpi_match);
+#endif
+
- Similar to FDT table
- Allows private data for “quirks”

---
Process Quirks
 static inline unsigned int s3c24xx_get_device_quirks(struct platform_device *pdev)
 {
+ struct acpi_handle *dev_handle;
+ struct acpi_device_id const *dev_id;
+
+ dev_handle = ACPI_HANDLE(&pdev->dev);
+
        if (pdev->dev.of_node) {
        const struct of_device_id *match;
        match = of_match_node(s3c24xx_i2c_match, pdev->dev.of_node);
        return (unsigned int)match->data;
        }
+ if (dev_handle) {
+ dev_id = acpi_match_device(s3c24xx_i2c_acpi_match, &pdev->dev);
+ return (unsigned int)dev_id->driver_data;
+ }
+
        return platform_get_device_id(pdev)->driver_data;
 }

---
Process Quirks
- Uses the ACPI match table
- Types are different but functionally same as FDT version
- Quirks should be rare on ACPI systems

---
+#ifdef CONFIG_ACPI
+/*
+ * ACPI resource callback
+ */
+static acpi_status
+s3c24xx_i2c_acpi_resource(struct acpi_resource *resource, void *context)
+{
+ u32 i;
+ struct s3c24xx_i2c *i2c = context;
+
+ switch (resource->type) {
+ case ACPI_RESOURCE_TYPE_EXTENDED_IRQ:
+ /* IRQ resources have already been read */
+ return AE_OK;
+
+ case ACPI_RESOURCE_TYPE_FIXED_MEMORY32:
+ /* Mem resources have already been read */
+ return AE_OK;
+
+ case ACPI_RESOURCE_TYPE_GPIO:
+ {
+ struct acpi_resource_gpio *p = &resource->data.gpio;
+
+ if (p->pin_table_length != 2) {
+ dev_err(i2c->dev, "2 GPIOS required in resource\n");
+ return AE_OK;
+ }
+
+ for (i = 0; i < p->pin_table_length; i++)
+ i2c->gpios[i] = p->pin_table[i];
+
+ return AE_OK;
+ }
+ default:
+ dev_info(i2c->dev, "Resource %d isn't MMIO, IRQ or GPIO\n",
+ resource->type);
+
+ case ACPI_RESOURCE_TYPE_END_TAG:
+ return AE_OK;
+ }
+ return AE_CTRL_TERMINATE;
+}

---
+static int s3c24xx_i2c_parse_acpi_gpio(struct s3c24xx_i2c *i2c)
+{
+ int idx, gpio, ret;
+ struct acpi_handle *dev_handle = ACPI_HANDLE(i2c->dev);
+
+ if (i2c->quirks & QUIRK_NO_GPIO)
+ return 0;
+
+ ret = acpi_walk_resources(dev_handle, METHOD_NAME__CRS,
+ s3c24xx_i2c_acpi_resource, i2c);
+ if (ACPI_FAILURE(ret)) {
+ pr_warn("Failure evaluating %s\n", METHOD_NAME__CRS);
+ return -EINVAL;
+ }
+
+ for (idx = 0; idx < 2; idx++) {
+ gpio = i2c->gpios[idx];
+ if (!gpio_is_valid(gpio)) {
+ dev_err(i2c->dev, "invalid gpio[%d]: %d\n", idx, gpio);
+ goto free_gpio;
+ }
+ i2c->gpios[idx] = gpio;
+
+ ret = gpio_request(gpio, "i2c-bus");
+ if (ret) {
+ dev_err(i2c->dev, "gpio [%d] request failed\n", gpio);
+ goto free_gpio;
+ }
+ }
+ return 0;
+
+free_gpio:
+ while (--idx >= 0)
+ gpio_free(i2c->gpios[idx]);
+ return -EINVAL;
+}

---
+static void s3c24xx_i2c_acpi_gpio_free(struct s3c24xx_i2c *i2c)
+{
+ unsigned int idx;
+
+ if (i2c->quirks & QUIRK_NO_GPIO)
+ return;
+
+ for (idx = 0; idx < 2; idx++)
+ gpio_free(i2c->gpios[idx]);
+}
+#else
+static int s3c24xx_i2c_parse_acpi_gpio(struct s3c24xx_i2c *i2c)
+{
+ return 0;
+}
+
+static void s3c24xx_i2c_acpi_gpio_free(struct s3c24xx_i2c *i2c)
+{
+}
+#endif

---
Processing the Resources
- In this example most resources processed by acpi-platform.c
- GPIO resources not represented by IO_RESOURCE structures so parsed in driver
- Resources passed from ASL as structures

---
+#ifdef CONFIG_ACPI
+/* s3c24xx_i2c_parse_acpi
+ *
+ * Parse the ACPI ASL and retreive the platform data.
+*/
+
+static void
+s3c24xx_i2c_parse_acpi(struct device *device, struct s3c24xx_i2c *i2c)
+{
+ struct s3c2410_platform_i2c *pdata = i2c->pdata;
+ struct acpi_handle *dev_handle = ACPI_HANDLE(device);
+ acpi_status res;
+ u64 result;
+
+ pdata->bus_num = -1; /* i2c bus number is dynamically assigned */
+
+ res = acpi_evaluate_integer(dev_handle, "DLAY", NULL, &result);
+ if (!ACPI_FAILURE(res))
+ pdata->sda_delay = result;
+
+ res = acpi_evaluate_integer(dev_handle, "SADD", NULL, &result);
+ if (!ACPI_FAILURE(res))
+ pdata->slave_addr = result;
+
+ res = acpi_evaluate_integer(dev_handle, "FREQ", NULL, &result);
+ if (!ACPI_FAILURE(res))
+ pdata->frequency = result;
+
+ dev_dbg(device, "ACPI delay %d, freq %ld, address %x\n",
+ pdata->sda_delay, pdata->frequency, pdata->slave_addr);
+}
+#else
+static void
+s3c24xx_i2c_parse_acpi(struct device_node *np, struct s3c24xx_i2c *i2c)
+{
+ return;
+}
+#endif

---
Process Misc Data
- Misc Data obtained by executing ASL methods
- This example just one way, could also have had one method return a structure of values

---
Probe
        struct s3c24xx_i2c *i2c;
        struct s3c2410_platform_i2c *pdata = NULL;
        struct resource *res;
+ struct acpi_handle *dev_handle;
        int ret;
- if (!pdev->dev.of_node) {
+ dev_handle = DEVICE_ACPI_HANDLE(&pdev->dev);
+
+ if (!pdev->dev.of_node && !dev_handle) {
        pdata = pdev->dev.platform_data;
        if (!pdata) {
        dev_err(&pdev->dev, "no platform data\n");
- Add checking of ACPI handle
- Handle will be set if probed from ACPI

---
Probe
        }
        i2c->quirks = s3c24xx_get_device_quirks(pdev);
- if (pdata)
+ if (pdata) {
        memcpy(i2c->pdata, pdata, sizeof(*pdata));
- else
- s3c24xx_i2c_parse_dt(pdev->dev.of_node, i2c);
+ } else {
+ if (pdev->dev.of_node)
+ s3c24xx_i2c_parse_dt(pdev->dev.of_node, i2c);
+ if (dev_handle)
+ s3c24xx_i2c_parse_acpi(&pdev->dev, i2c);
+ }
        strlcpy(i2c->adap.name, "s3c2410-i2c", sizeof(i2c->adap.name));
        i2c->adap.owner = THIS_MODULE;
Add calls to parse data from ASL

---
Probe
        if (i2c->pdata->cfg_gpio) {
        i2c->pdata->cfg_gpio(to_platform_device(i2c->dev));
+ } else if (dev_handle) {
+ s3c24xx_i2c_parse_acpi_gpio(i2c);
        } else if (IS_ERR(i2c->pctrl) && s3c24xx_i2c_parse_dt_gpio(i2c)) {
        return -EINVAL;
        }
Parse GPIO resources from ASL

---
ACPI Match Table
        .name = "s3c-i2c",
        .pm = S3C24XX_DEV_PM_OPS,
        .of_match_table = of_match_ptr(s3c24xx_i2c_match),
+ .acpi_match_table = ACPI_PTR(s3c24xx_i2c_acpi_match),
        },
 };
Add the acpi match table to platform_driver structure

---
Conclusion
- ACPI similar to work already done for FDT
- Actual driver code will depend on ASL from OEMs